## Slide 1
The Design and Simulation of a Digital Data Transmission Error Detection System
XOR
DATA
CHECK
Title : Digital Data Transmission Error Detection System
Team members:
Nihal Rahas : 2620030197
Sandeep : 2620090082
Manzar : 2620030203
Rithesh : 2620030439
Guide: Dr. Venkanna Isampalli
Department of Freshman Engineering Department
Koneru Lakshmaiah Education Foundation
Academic Year : 2026-27

## Slide 2
Introduction
DIGITAL LOGIC • PROJECT INTRODUCTION
Digital Data Transmission Error Detection System
Digital data is transmitted as binary bits (0s and 1s).
Noise or interference during transmission can change a bit and corrupt the received data.
This project uses XOR gates and parity checking to detect possible transmission errors.
A parity bit is added at the transmitter and checked at the receiver to indicate whether the parity condition is satisfied.
XOR
DATA
CHECK

## Slide 3
Why error detection matters
Digital information travels as bits — 0s and 1s. During transmission, noise or interference can flip a bit and change the message.
SENT: 1 0 1 1
RECEIVED: 1 0 0 1
One bit changed in transit
PROJECT GOAL
Build and simulate a simple parity-based circuit that flags whether received data may contain an error.
DIGITAL LOGIC • PROJECT PRESENTATION
10-SLIDE PRESENTATION

## Slide 4
Parity checking in one minute
A parity bit is an extra bit added to a data word so the total number of 1s follows a chosen rule.
EVEN PARITY
Choose the parity bit so the total count of 1s is even.
Example: data 1011 has three 1s Parity bit = 1 → 10111 has four 1s
ODD PARITY
Choose the parity bit so the total count of 1s is odd.
Example: data 1011 has three 1s Parity bit = 0 → 10110 has three 1s
This project demonstrates even parity; the same method can be adapted for odd parity.
DIGITAL LOGIC • PROJECT PRESENTATION

## Slide 5
Why use the XOR gate?
XOR outputs 1 when its inputs are different, and 0 when they are the same. Cascaded XOR gates calculate parity.
A
B
A ⊕ B
0
0
0
0
1
1
1
0
1
1
1
0
A ⊕ B
0 / 1
XOR is also called modulo-2 addition.
Parity bit for D3 D2 D1 D0 (even parity): P = D3 ⊕ D2 ⊕ D1 ⊕ D0
DIGITAL LOGIC • PROJECT PRESENTATION

## Slide 6
Transmitter-to-receiver block diagram
DATA INPUT
XOR PARITY GENERATOR
TRANSMISSION CHANNEL
XOR PARITY CHECKER
STATUS
At the sender, the parity generator appends one bit. At the receiver, the checker evaluates the received data and parity bit.
Checker output 0 → parity condition satisfied
Checker output 1 → error detected
DIGITAL LOGIC • PROJECT PRESENTATION

## Slide 7
Parity generator and checker
Example: 4-bit data = 1 0 1 1
D3 D2 D1 D0
P = XOR of bits
Transmit 10111
For 1011, there are three 1s. Even parity requires P = 1, so the transmitted word has four 1s.
Receiver XORs all 5 received bits
0 = parity OK | 1 = error flag
DIGITAL LOGIC • PROJECT PRESENTATION

## Slide 8
Test cases and expected results
Case
Sent word
Received
Checker
Result
1
10111
10111
0
Parity OK
2
10111
10011
1
Error flagged
3
10111
00111
1
Error flagged
4
10111
10001
0
Not detected*
*Two bits flipped in case 4, so even parity remains unchanged. Parity detects any odd number of bit flips, but may miss an even number.
DIGITAL LOGIC • PROJECT PRESENTATION

## Slide 9
Simulation workflow
01
Design
Place XOR gates and connect data inputs.
02
Generate
Cascade XOR gates to produce the parity bit.
03
Check
Connect received data and parity to the checker.
04
Test
Apply input combinations and observe the output.
Suggested tools: Logisim Evolution or another digital logic simulator.
DIGITAL LOGIC • PROJECT PRESENTATION

## Slide 10
What the project demonstrates
WHAT WORKS
XOR gates generate and verify parity with a small, easy-to-follow circuit.
WHAT IT CAN'T DO
Parity does not identify which bit changed and cannot correct the data.
KEY LIMIT
An even number of bit flips can go undetected; parity is a basic error-detection method.
Conclusion
The simulation shows how a simple logic-gate circuit can add a useful integrity check to digital communication.
DIGITAL LOGIC • PROJECT PRESENTATION

## Slide 11
THANK YOU
Questions & Discussion
Digital Data Transmission • XOR Parity Error Detection